## Slide 1
Telekomunikasi
MODULASI DIGITAL

## Slide 2
Modulasi Digital
Teknik modulasi digital pada prinsipnya merupakan variant dari metode modulasi analog
Teknik modulasi digital :
    Teknik dasar :
      Amplitude shift keying (ASK)
      Frequency shift keying (FSK)
      Phase shift keying (PSK)
    Variant dari teknik dasar di atas :
      4 Pulse Amplitude Modulation (4-PAM)
      Quadrature Phase Shift Keying (QPSK)
      Quadrature Amplitude Modulation (QAM)

## Slide 3
Sinyal direpresentasikan dalam dua kondisi perubahan amplitudo gelombang pembawa
  Sinyal “1”  direpresentasikan dengan status “ON” (ada gelombang pembawa)
  Sinyal “0”  direpresentasikan dengan status “OFF” (tidak ada gelombang pembawa)
Sinyal direpresentasikan dalam perubahan frekuensi gelombang pembawa
  Sinyal “1”  direpresentasikan dengan frekuensi tinggi
  Sinyal “0”  direpresentasikan dengan frekuensi rendah
Sinyal direpresentasikan dalam perubahan phase gelombang pembawa
  Sinyal “1”  Phase gelombang pembawa tidak bergeser (pergeseran phase 00)
  Sinyal “0”  Phase gelombang pembawa bergeser 1800 (berlawanan)
Binary Amplitude Shift Keying (BASK)
BASK, BFSK dan BPSK
Binary Frequency Shift Keying (BFSK)
Binary Phase Shift Keying (BPSK)

## Slide 4
BASK, BFSK dan BPSK
BASK
BFSK
BPSK
Signal

## Slide 5
Sinyal direpresentasikan dengan 4 nilai besaran amplitudo dari gelombang pembawa.
4 Pulse Amplitude Modulation (4-PAM)
Bit value | Amplitude
00 | -2
01 | -1
10 | +1
11 | +2
00
01
10
11
+1
+2
-1
-2

## Slide 6
Sinyal direpresentasikan dengan 4 status pergeseran phase dari gelombang pembawa.
Quadrature Phase Shift Keying (QPSK)
Bit value | Phase shift
00 | 00
01 | +900
10 | -900
11 | 1800
00
+900
-900
00
01
10
11

## Slide 7
Quadrature Amplitude Modulation (QAM)
Merupakan kombinasi amplitude modulation dan phase shift keying
Sinyal direpresentasikan dalam kombinasi besaran amplitudo (2 besaran) dan pergeseran phase (4 status).
Memungkinkan kecepatan yang lebih tinggi untuk bandwidth yang ditentukan
Lebih tahan terhadap noise
Bit value | Amplitude | Phase shift
000 | 1 | 00
001 | 2 | 00
010 | 1 | 900
011 | 2 | 900
100 | 1 | 1800
101 | 2 | 1800
110 | 1 | 2700
111 | 2 | 2700
00
900
1800
2700
1
2
000
001
010
011
100
101
110
111

## Slide 8
Bit stream sinyal sbb : 001010100011101000011110
Bagi dalam kelompok masing-masing 3 bit: 001-010-100-011-101-000-011-110
Quadrature Amplitude Modulation (QAM)
Contoh :
Bit value | Amplitude | Phase shift
001 | 2 | 00
010 | 1 | 900
100 | 1 | 1800
011 | 2 | 900
101 | 2 | 1800
000 | 1 | 00
011 | 2 | 900
110 | 1 | 2700
Perubahan amplitudo dan phase
Bentuk gelombang modulasi

## Slide 10: WHAT IS MODULATION?
Encoding information in a manner
suitable for transmission.
Translate baseband source signal to bandpass signal
Bandpass signal: “modulated signal”
How?
  Vary amplitude, phase or frequency of a carrier
Demodulation: extract baseband message from carrier

## Slide 11: Contoh modulasi Digital
ASK
FSK
PSK
DSB

## Slide 12: Cont’ Contoh modulasi Digital
0
1
2
3
4
5
6
7
8
4 ASK
Compare Different Modulation Methods to transmit [1 0 1 1 0 0 0 1]
1
0
-1
0
1
2
3
4
5
6
7
8
1
0
-1
QPSK
10 ->  /2
0
1
2
3
4
5
6
7
8
1
0
-1
16 QAM
0
1
2
6
7
8
1
0
-1
binary FSK
3 4 5
Symbol Interval (Ts)
11 -> 3
/200 -> 0
01 -> 

## Slide 13
AMPLITUDE SHIFT KEYING (ASK) MODULATION
c
i
cos t   
2Ei
T
s (t) 
1 c
T
ai  Ei
 (t)  2 cos t   
si (t)  ai1 (t) i  1,…, M
1
 (t)
s1
E1
“0”
s2
0
“1”
On-off keying (M=2):

## Slide 14: M-ary ASK
M-ary ASK sering disebut M-ary Pulse Amplitude modulation (M-PAM)
T
c
2 cos t 
si (t)  ai
i g
i
Eg
T
2
2
1
(M 2 1)
3
Es 
c
ai  (2i 1 M ) Eg
E  s  E 2i 1 M 
2 cos t 
 (t) 
si (t)  ai1 (t) i  1,…, M
4-ASK = 4-PAM:
 (t)
s1 s2
0
3 Eg
s4
s3
“00” “01” “11”
“10”
Eg
Eg
1
3 Eg

## Slide 15: ERROR PROBABILITY

T
0
1 (t)
(
ML detector
Compare with M-1 thresholds)
r(t)
r1
mˆ
1
 (t)
0
3 Eg
“00”
“01”
s4
s3
“11”
“10”
s1 s2
Eg
Eg
3 Eg
4-PAM

## Slide 16: ERROR PROBABILITY (CONT’)






0 
M 2 1 N
Q
M
P (M )  2(M 1)
6log2 M Eb
E

## Slide 17: Probability of symbol error for M-PAM
PE
Eb / N0 dB
Note!
M = 2k
“The same average symbol energy for different sizes of signal space”

## Slide 18: Signal Space of several modulation

## Slide 19
Section Break
Insert the Sub Title of
Your Presentation

## Slide 20
BINARY SHIFT KEYING

## Slide 21: Binary Shift Keying (BPSK)
🞇 Perubahan Parameter Fasa dari sinyal pembawa sesuai dengan
sinyal informasi.
🞇 Menggunakan alternatif-alternatif fasa gelombang sinus utk mengkodekan bit-bit dimana Fasa dipisahkan 180 derajat
🞇 Sederhana utk diimplementasikan, tidak efisien dalam penggunaan bandwidth.
🞇 Sangat kokoh, sering digunakan secara extensif pada komunikasi satelit.

## Slide 22: Blok Sistem BPSK

c
 Acos(2f t   ); b(t ) "0"
s(t )   Acos(2fc t  0); b(t ) "1"

## Slide 23: Contoh Sinyal BPSK
Data
Carrier
Carrier+ 
BPSK waveform
1 1 0
1
0
1

## Slide 24: Konstelasi sinyal BPSK
🞇 Fasa dipisahkan 180 derajat.
binary '1'
s1 (t)  Ac cos(2fc t)
s2 (t)  Ac cos(2fc t   ) binary '0'
Q
0
State
1
State

## Slide 25: Spektrum Sinyal BPSK
f
S(f)
fc fc+ R
fc- R
fc+ 2R
fc- 2R
BWmin
BWmin=2BN
= 2.Rb/2
BN=Bandwidth Nyquist

## Slide 26
MODULASI QPSK (QUADRATURE
SHIFT KEYING)

## Slide 27: Quadrature Phase Shift Keying
Teknik modulasi multilevel : 2 bit per symbol
Lebih efisien spektrum, lebih kompleks receiver.
Dua kali lebih efisien bandwidth daripada BPSK
Q
00 State
Phase of Carrier: /4, 3/4, 5/4, 7/4
11 State
10 State
01 State

## Slide 28: 4 bentuk gelombang berbeda:
.5
.5
1
.5
0
.5
-1
.50
.5
1
.5
0
.5
-1
.50
0.2 0.4 0.6 0.8 1
1
.5
0
.5
-1
.50
.5
1
.5
0
.5
-1
.50
0.2 0.4 0.6 0.8 1
cos+sin
00
-cos+sin
01
0.2 0.4 0.6 0.8 1
cos-sin
10
0.2 0.4 0.6 0.8 1
-cos-sin
11
Bentuk Sinyal
QPSK
28

## Slide 29: Blok Sistem QPSK
29

## Slide 30
Bandpass modulation: Signal Space & Vector
🞇 Bandpass modulation: The process of converting data signal to a sinusoidal waveform where its amplitude, phase or frequency, or a combination of them, is varied in accordance with the transmitting data.
🞇 Bandpass signal (General Condition):
🞇 We assume here (otherwise will be stated):
🞇 is a rectangular pulse shape with unit energy.
🞇 Gray coding is used for mapping bits to symbols.
🞇 denotes average symbol energy given by
i
0  t  T
2Ei
T
s (t )  h(t )
cosc t  (i  1)t  i (t )
where h(t) is the baseband pulse shape with eneErgh y .
s
E

30
M
i
s
E
M
E 
i1
1
h(t)

## Slide 31: Phase Shift Keying (PSK)
I. PSK signal waveform (transmitted signal):
0  t  T , i  1, , M ,
2 2
i
, , , 0 or
si (t)  2E cos[0t  i (t)], phase: i (t)  2i ,
T M
🞇 Phase (examples):
BPSK(M  2) : i  , 0
 3

 3 5
7 7 / 2
QPSK(M  4) :  

 
, , 4 , 4 


 4 4
i1/ 2
2
T
0
i
s (t)dt ?
🞇 Symbol energy and symbol interval
E is symbol energy. T is symbol interval.
Can you show that E 

31

## Slide 32: II. Signal space representation
1) Orthonormal basis:
2) Signal vector:
M
E cos 2i ,  E sin 2i ,
i 
M 



i  1, , M
si (t) : s 
1(t)  2 cos(0t), 2 (t)  2 sin(0t)
T T
Note: decomposition of PSK signal waveform:
si (t)  2E cos[i (t)]cos(0t)  2E sin[i (t)]sin(0t)
T T
3) Constellations:
(examples)
32

## Slide 33: Signal space representation (cont.)
4) A proof of signal space representation
🞇 Bases are orthonormal
🞇 Signal space vector for each waveform si(t)
15
2
0
2
2
2
2
0
0
0
1
0
1
2
0
0
0
0
T
0
T
0
T T
T
0
T
0
2 T sin (
(t)dt
 t) sin(
 (t)dt
 (t)
 (t)dt







 2 T cos (
 t)]/ 2dt  1.
 t)dt  2 T [1 cos(2
 2 T cos(
 t)]/ 2dt  1.
 t)dt  2 T sin(2
[1 cos(2
 t) / 2dt  0.
 t)dt  2 T









0
0
i1
i 1
i2
i 2
0 i 0
T
0
i
0 i
i
i
0 i i
T
0
0 i 0
a   s (t) (t)dt  2
E T T cos[ t   (t)]sin( t)dt
 E T sin[
a   s (t) (t)dt  2 E T T cos[ t   (t)]cos( t)dt
 E T cos[
(t)]dt  E cos[ (t)]
 (t)]  cos[2
 t  
 t  
 (t)]  sin[2






(t)]dt   E sin[ (t)]

## Slide 34
Signal space representation (cont.)
5) What happens if baseband pulse-shaping h(t) is considered?
🞇 Signal waveform:
🞇 Use basis (note that h(t) can be assumed normalized):
🞇 Signal space vector is still:
🞇 Conclusion: there is no difference in signal space whether pulse-shaping is considered. We can study only PSK instead of the more general PM.
T
T
2 h(t)sin(0t)
1(t)  2 h(t) cos(0t),
2 (t) 
i
M

E cos 2i ,  E sin 2i ,

M 
 
i  1, , M
si (t) : s 
T
si (t)  2E h(t) cos[0t  i (t)]
34

## Slide 35: PSK modulator
🞇 General cas
e: M
-ary PSK modulator
ai  E
h(t)
2 T cos(0t)
🞇 Special case: BPSK modulator
si (t)
binary
bits
ai1
ai2
h(t)
h(t)
0
2 T cos( t)
2 T sin(0t)
si (t)
Note:
Inputs are signal- space vector.
Carriers are in basis form.
si (t)  ai1 2 T cos(0t)  ai2 2 T sin(0t)
si  (ai1, ai2 )   E cos(2 i M ),  E sin(2 i M )
Symbol map
35

## Slide 36: Bandwidth of PSK signal waveform
🞇 Just like DSB modulation:
18
WPSK  2Wbaseband
🞇 Exercise : Consider QPSK transmission with date rate 2000 bps. The magnitude of the signal si(t) is √2E/T
=1 volt.
What is the minimum PSK signal bandwidth?
Find the signal space points
Draw the constellation
Find signal waveform for transmitting {1001}.
a) Rs  Rb (log2 M )  2000 / 2  1000. WPSK  2Wbaseband,min  2 Rs 2  1000Hz.
i  1, , 4
b) si  ( E cos 2 i 4,  E sin 2 i 4), where E  T / 2  0.5103, d) Define mapping as: {00:0, 01: , 10: 2, 11: 3 2}.
Then {10}  s1(t)  cos(0t   2). {01}  s2 (t)  cos(0t   )
Phase i (t) in si (t) is different from phase of si (phase in signal space)

## Slide 37
Demodulation and detection
Demodulation: The receiver signal is converted to baseband, filtered and sampled.
Detection: Sampled values are used for detection using a decision
rule such as ML detection rule.
19
 
zN 
 z 
⁝
1
 
 z

0
1(t)

T
0
N
 (t)
r(t)
T z1
zN
z
Decision circuits
(ML detector)
mˆ
Demodulation
Detection

## Slide 38: Demodulations type:
20
Modulatio n | Varying parameter | Demodulation
PSK |  (t) | Coherent or noncoherent
QAM | both A(t) and (t) | Coherent or noncoherent
FSK | 0 | Coherent or Noncoherent
🞇 Some notations
🞇 Carrier: s(t)  A(t) cos[0t  (t)], 0  2 f0
🞇 Modulation types with respect to carrier parameters

## Slide 39: Two dimensional modulation, demodulation and detection (M-PSK)
21


 M 
c
i
cos t  2i 
2Es
T
s (t) 
1
i
i 2 s
i1 s
c 2 c
T T
Es  Ei  s
 M 
 
 M 
 
2
a  E sin 2i 
a  E cos 2i 
2 cos t   (t)  2 sin t 
 (t) 
🞇 M-ary Phase Shift Keying (M-PSK)
si (t)  ai11 (t)  ai 2 2 (t) i  1,…, M

## Slide 40: Two dimensional mod… (MPSK)
1(t)
Eb
“0”
s1
“1”
s2
Eb
3
s
s7
1(t)
s4
s2
Es
“000”
s6
s8
1
s
“110”
s5
“001”
“011”
“010”
“101”
“111”
“100”
2
1
s
E
“00” s
“11”
 2 (t)
2s2 3
1(t)
s4
“10”
s “01”
QPSK (M=4)
BPSK (M=2)
 2 (t)
8PSK (M=8)
 2 (t)

## Slide 41
Demodulation BPSK
23

T
0
r(t)
Decision Circuits Compare z with threshold.
mˆ
1(t)
z
1(t)
Eb
🞇 BPSK with coherent detection:
“0”
s1
“1”
s2
Eb
 2 Eb
s1  s2

## Slide 42
Error probability …
🞇 BPSK with coherent detection (with perfect carrier
24
0





N
2E 
b 
PB  Q



 
N0 / 2
PB  Q
 s1  s2 / 2 
1
 (t)
Eb
b
E
0
s1
s2
pz (z | m1)
synchronization):
pz (z | m2 )

## Slide 43: Demodulation M-PSK
🞇 Coherent detection of Q-PSK
25
Decision Region QPSK
decide s3
s3
decide s1
1(t)
s1
 2 (t)
decide s2 s2





 


















0
0 
0 
decide s4 s4
 2
0 
2
1
2
1 
N
N
Q
N
N
 1  Q
p  1  p
2Eb
pe  Q
2Eb
2Eb
pe  1  pc  2Q
2Eb
BPSK  I
C

## Slide 44: Power Spectra of M-Ary PSK
B
B
b b 2
2
2
2E log M sin c T f log M 
S  f   2E sin c Tf 
S  f  
44

## Slide 45: QPSK vs. BPSK
🞇 Let’s compare the two based on BER and bandwidth
BPSK
BER Bandwidth
QPSK
BPSK
Rb
QPSK
Rb/2
EQUAL
0





N
2E 
b 
PB  Q
0
45





N
2E 
b 
PB  Q

## Slide 46
Error probability …
🞇 Coherent detection
of M-PSK
28
8-PSK
s3
1
 (t)
4
2
Es
s6
s8
1
s“000”
“s001”
 2 (t)
“011”
“0s10”
“101” s7
“110”
s5
“111”
“100”
Decision variable
z  ˆ  r
Choose
smallest
X
arctan Y
ˆ
Compute
| i ˆ |

T
0
1(t)

T
0
 2 (t)
r(t)
T
0
r1  X   r(t).1 (t)dt
mˆ
T
r2  Y   r(t).2 (t)dt
0
ˆ
 is a noisy estimate of the transmittedi

## Slide 47: Error probability …
🞇 Coherent detection of MPSK …
🞇 The detector compares the phase of observation vector to M-1 thresholds.
🞇 Due to the circular symmetry of the signal space, we
have:
where
🞇 It can be shown that (for M > 4)
29
M
M
E C
p ()d
 / M
ˆ
 / M

m1
P (M )  1 P (M )  1 1
Pc (sm )  1 Pc (s1 )  1





 M 
  
sin
2Es
PE (M )  2Q
N0





 M 
  
b sin
2log M E
PE (M )  2Q
2
N0
or
0

2
ˆ
|  |

 0
 
N
E
 N
2 E
p () 
s cos() exp  s sin2  ;

## Slide 48: Probability of symbol error for M- PSK
30
PE
Eb / N0 dB
Note!
M = 2k
“The same average symbol energy for different sizes of signal space”

## Slide 49
Terimakasih

## Slide 50
Terimakasih