## Slide 1: Network Governance SESSION 1 - Analyzing Business and Technical Requirements
D5727 – Dr. Eng. Nico Surantha, ST., MT.

## Slide 2: Outline
Analyzing business goals and constraints
Analyzing technical goals and tradeoffs

## Slide 3: Top-Down Network Design
Network design should be a complete process that matches business needs to available technology to deliver a system that will maximize an organization’s success
  In the LAN area it is more than just buying a few devices
  In the WAN area it is more than just calling the phone company

## Slide 4: Start at the Top
Don’t just start connecting the dots
Analyze business and technical goals first
What is the business constraints?
  Budgets, limited working personnel, tight timeframes
Explore divisional and group structures to find out who the network serves and where they reside
Determine what applications will run on the network and how those applications behave on a network
Focus on Layer 7 and above first
Obtain the big picture first, detail later
Notes: Layer 8 of the OSI model encompasses office politics, budgets, training, and other human factors.

## Slide 5: Layers of the OSI Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Layer 1
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2

## Slide 6: Structured Design
The system is designed in a top-down sequence
A focus is placed on understanding data flow, data types, and processes that access or change the data.
A focus is placed on understanding the location and needs of user communities that access or change data and processes.
Several techniques and models can be used to characterize the existing system, new user requirements, and a structure for the future system.
A logical model is developed before the physical model.
  The logical model represents the basic building blocks, divided by function, and the structure of the system.
  The physical model represents devices and specific technologies and implementations.

## Slide 7: Systems Development Life Cycles
SDLC: Does it mean Synchronous Data Link Control or Systems Development Life Cycle?
The latter for the purposes of this class!
Typical systems are developed and continue to exist over a period of time, often called a systems development life cycle (SDLC)

## Slide 8: Top-Down Network Design Steps
Analyze requirements
Develop logical design
Develop physical design
Test, optimize, and document design
Monitor and optimize network performance
Implement and test network

## Slide 9: Network Design Steps
Phase 1 – Analyze Requirements
  Analyze business goals and constraints
  Analyze technical goals and tradeoffs
  Characterize the existing network (protocol behavior, QoS requirements)
  Characterize network traffic

## Slide 10: Network Design Steps (2)
Phase 2 – Logical Network Design
  Design a network topology
  Design models for addressing and naming
  Select switching and routing protocols
  Develop network security strategies
  Develop network management strategies
  Which service providers can meet WAN and remote access requirements.

## Slide 11: Network Design Steps (3)
Phase 3 – Physical Network Design
  Select technologies and devices to realize the logical design
Phase 4 – Testing, Optimizing, and Documenting the Network Design
  Test the network design
  Optimize the network design
  Document the network design

## Slide 12: The PDIOO Network Life Cycle
Plan
Design
Implement
Operate
Optimize
Retire
Plan:
Network requirement
Area where network will be installed
Identificaiton of users
Design :
- Logical and physical design
Implementation
- Building designs according to specifications
Operate:
Final testing of design
Provide input for optimization
optimize
Identifies and resolves problem
Network redesign (if too many problem or if requirement changes)
Retire:
- Changes network or devices
Notes: Plan :
Network requirements
Area where network will be installed
Identification of users who will require a network device
Design:
Logical and physical design
Implementation
The network is built according to design specifications
Operate:
The final test of the efficiency of design
Provide input for optimize
Optimize:
Identifies and resolves problem
Network redesign (if too many problem or if requirement changes)
Retire:
- When the network or devices retire, taken out from production

## Slide 13: Business Goals
Increase revenue
Reduce operating costs
Improve communications
Shorten product development cycle
Expand into worldwide markets
Build partnerships with other companies
Offer better customer support or new customer services

## Slide 14: Recent Business Priorities
Mobility
Security
Resiliency (fault tolerance)
Business continuity after a disaster
Network projects must be prioritized based on fiscal goals
Networks must offer the low delay required for real-time applications such as VoIP
Notes: Resiliency means how much stress a network can handle and how quickly the network can rebound from problems, including security breaches, natural and unnatural disasters, human error, and catastrophic software or hardware failures.
Some experts, including Howard Berkowitz, have a mild dislike of the word “resiliency” as it sounds too much like a stretched rubber band or a trampoline. As Berkowitz says in his excellent book, WAN Survival Guide (Wiley 2001), “I avoid designing networks that stretch too far, bounce up and down, or oscillate between normal and backup states.”
So he likes “fault tolerance,” but he points out that it does not mean “immune to any conceivable threat.” Berkowitz states that, “A sufficient quantity of explosives can overcome the tolerance of any network.” :-)

## Slide 15: Business Constraints
Politics and policies
  Who wants the project to fail for any reason?
  How they call a design testing is done?
  Existing network policies
  Who is the decision makers
Budget
  Who controls the budget?
  Develop ROI analysis of network design with customer
Notes: For example when you try to merge voice and data network

## Slide 16: Business Constraints (2)
Staffing
  What the level of in-house expertise?
  Do we need to outsource
Schedule
Notes: For example when you try to merge voice and data network

## Slide 17: Collect Information Before the First Meeting
Before meeting with the client, whether internal or external, collect some basic business-related information
Such as
  Products produced/Services supplied
  Financial viability
  Customers, suppliers, competitors
  Competitive advantage

## Slide 18: Meet With the Customer

## Slide 19: Meet With the Customer
Try to get
  A concise statement of the goals of the project
    What problem are they trying to solve?
    How will new technology help them be more successful in their business?
    What must happen for the project to succeed?
    What is the criteria of success?
      Operational saving? Increasing revenue? Builds partnership?

## Slide 20: Meet With the Customer
What will happen if the project is a failure?
  Is this a critical business function?
  Is this project visible to upper management?
  Who’s on your side?

## Slide 21: Meet With the Customer
Discover any biases
  For example
    Will they only use certain company’s products?
    Do they avoid certain technologies?
    Do the data people look down on the voice people or vice versa?
  Talk to the technical and management staff

## Slide 22: Meet With the Customer
  Get a copy of the organization chart
    This will show the general structure of the organization
    It will suggest users to account for
    It will suggest geographical locations to account for
Notes: Learn about the organizational structure
Your internetwork design reflects the corporate structure
Who can approve your network design

## Slide 23: Meet With the Customer
  Get a copy of the security policy
    How does the policy affect the new design?
    How does the new design affect the policy?
    Is the policy so strict that you (the network designer) won’t be able to do your job?
  Start cataloging network assets that security should protect
    Hardware, software, applications, and data
    Less obvious, but still important, intellectual property, trade secrets, and a company's reputation

## Slide 24: The Scope of the Design Project
Small in scope?
  Allow sales people to access network via a VPN
Large in scope?
  An entire redesign of an enterprise network
Use the OSI model to clarify the scope
  New financial reporting application versus new routing protocol versus new data link (wireless, for example)
Does the scope fit the budget, capabilities of staff and consultants, schedule?

## Slide 25: Gather More Detailed Information
Applications
  Now and after the project is completed
  Include both productivity applications and system management applications
User communities
Data stores
Protocols
Current logical and physical architecture
Current performance
Notes: User communities, data stores, protocols, and the current architecture and performance will be discussed in the next few chapters. This chapter focuses on business needs and applications, which should be the first area of research in a top-down network design project. Network design is iterative, however, so many topics are addressed more than once as the designer gathers more detailed information and conducts more precise planning. So, gaining a general understanding of the size and location of user communities, for example, might be appropriate at this stage of the design project, but user communities should be investigated again when characterizing network traffic.

## Slide 26: Network Applications
Name of Application
Type of Application
New Application?
Criticality
Comments

## Slide 27: Analyzing technical goals and tradeoffs
  Scalability
  Availability
  Network performance
  Security
  Manageability
  Usability

## Slide 28: Scalability
Scalability refers to the ability to grow
Some technologies are more scalable
  Flat network designs, for example, don’t scale well
Try to learn
  Number of sites to be added
  What will be needed at each of these sites
  How many users will be added
  How many more servers will be added

## Slide 29: Availability
Availability can be expressed as a percent uptime per year, month, week, day, or hour, compared to the total time in that period
  For example:
    24/7 operation
    Network is up for 165 hours in the 168-hour week
    Availability is 98.21%
Different applications may require different levels
Some enterprises may want 99.999% or “Five Nines” availability
Resiliency?

## Slide 30: Availability Downtime in Minutes
4.32
1.44
.72
.01
30
10
5
.10
1577
99.70%
526
99.90%
263
99.95%
5
99.999%
Per Hour
Per Day
Per Week
Per Year
.18
.06
.03
.0006
.29
2
105
99.98%
.012
Notes: 99.70% availability sounds pretty good, but it could mean that the network is down for 0.18 minutes every hour. This is 11 seconds. If those 11 seconds were spread out over the hour, nobody would notice possibly. But if there were some bug, for example, that caused the network to fail for 11 seconds every hour on the hour, people would notice. Users these days are very impatient.
Notice that 99.70% availability also could mean one catastrophic problem caused the network to be down for 1577 minutes all at once. That’s 26 hours. If it were on a Saturday and the network was never down for the rest of the year, that might actually be OK. So, you have to consider time frames with percent availability numbers.
Consider the holy grail: 99.999% availability. That’s 5 minutes downtime per year! Be sure to explain to the customer that scheduled maintenance and upgrades don’t count! Either that or plan for a network with triple redundancy (that could be extremely expensive to implement and operate).

## Slide 31: 99.999% Availability May Require Triple Redundancy
Can the customer afford this?
Enterprise
ISP 1
ISP 2
ISP 3
Notes: In the event of failure of the primary router, the secondary becomes the primary and still has a backup. Fix the previous primary and have it become the tertiary.
This helps with maintenance too. Pull out the tertiary and upgrade it. The primary still has a backup. After extensive testing, put the tertiary back in as the primary. Pull out the original primary and upgrade it. Put it back as the secondary. Finally pull out the original secondary and upgrade it.
Of course, the picture brings up all sorts of other questions because it uses an ISP example.
  Does the customer have provider independent addressing?
  Does the customer have an autonomous system number?
  Are the ISPs really independent? Is there true circuit diversity?
  Are the speeds the same on the three links to the ISPs so that performance degradation is minimized during upgrades or failures?
  Can load balancing be used when all three routers are operational?
  What are the routing protocols inside the enterprise network? Can traffic really get to all three routers, regardless of failures inside the enterprise network? Can the routing protocols adjust to changes?
  Will traffic flow out the “closest” router? Will traffic come in from the Internet via the “closest” entry?
Instructor note: The slide is not meant to be a design recommendation! It’s just a slide to get a discussion going on the ramifications of 99.999% availability.

## Slide 32: Availability
Availability can also be expressed as a mean time between failure (MTBF) and mean time to repair (MTTR)
Availability = MTBF/(MTBF + MTTR)
  For example:
    The network should not fail more than once every 4,000 hours (166 days) and it should be fixed within one hour
    4,000/4,001 = 99.98% availability

## Slide 33: Network Performance
Common performance factors include
  Bandwidth
  Throughput
  Bandwidth utilization
  Offered load
  Accuracy
  Efficiency
  Delay (latency) and delay variation
  Response time

## Slide 34: Bandwidth Vs. Throughput
Bandwidth and throughput are not the same thing
Bandwidth is the data carrying capacity of a circuit
    Usually specified in bits per second
Throughput is the quantity of error free data transmitted per unit of time
    Measured in bps, Bps, or packets per second (pps)

## Slide 35: Bandwidth, Throughput, Load
Offered Load
Throughput
Actual
Ideal
100 % of Capacity
100 % of Capacity

## Slide 36: Other Factors that Affect Throughput
The size of packets
Inter-frame gaps between packets
Packets-per-second ratings of devices that forward packets
Client speed (CPU, memory, and HD access speeds)

## Slide 37: Other Factors that Affect Throughput (2)
Server speed (CPU, memory, and HD access speeds)
Network design
Protocols
Distance
Errors
Time of day, etc., etc., etc.

## Slide 38: Throughput Vs. Goodput
You need to decide what you mean by throughput
Are you referring to bytes per second, regardless of whether the bytes are user data bytes or packet header bytes
  Or are you concerned with application-layer throughput of user bytes, sometimes called “goodput”
    In that case, you have to consider that bandwidth is being “wasted” by the headers in every packet

## Slide 39: Performance (continued)
Efficiency
  How much overhead is required to deliver an amount of data?
  How large can packets be?
    Larger better for efficiency (and goodput)
    But too large means too much data is lost if a packet is damaged
    How many packets can be sent in one bunch without an acknowledgment?

## Slide 40: Efficiency
Small Frames (Less Efficient)
Large Frames (More Efficient)

## Slide 41: Delay from the User’s Point of View
Response Time
  A function of the application and the equipment the application is running on, not just the network
  Most users expect to see something on the screen in 100 to 200 milliseconds

## Slide 42: Delay from the Engineer’s Point of View
Propagation delay
  A signal travels in a cable at about 2/3 the speed of light in a vacuum
Transmission delay (also known as serialization delay)
  Time to put digital data onto a transmission line
    For example, it takes about 5 ms to output a 1,024 byte packet on a 1.544 Mbps T1 line
Packet-switching delay
Queuing delay

## Slide 43: Queuing Delay and Bandwidth Utilization
Number of packets in a queue increases exponentially as utilization increases

## Slide 44: Example
A packet switch has 5 users, each offering packets at a rate of 10 packets per second
The average length of the packets is 1,024 bits
The packet switch needs to transmit this data over a 56-Kbps WAN circuit
  Load = 5 x 10 x 1,024 = 51,200 bps
  Utilization = 51,200/56,000 = 91.4%
  Average number of packets in queue =
    (0.914)/(1-0.914) = 10.63 packets

## Slide 45: Delay Variation
The amount of time average delay varies
  Also known as jitter
Voice, video, and audio are intolerant of delay variation
So forget everything we said about maximizing packet sizes
  There are always tradeoffs
  Efficiency for high-volume applications versus low and non-varying delay for multimedia

## Slide 46: Security
Focus on requirements first
Detailed security planning later
Identify network assets
  Including their value and the expected cost associated with losing them due to a security problem
Analyze security risks

## Slide 47: Network Assets
Hardware
Software
Applications
Data
Intellectual property
Trade secrets
Company’s reputation

## Slide 48: Security Risks
Hacked network devices
  Data can be intercepted, analyzed, altered, or deleted
  User passwords can be compromised
  Device configurations can be changed
Reconnaissance attacks
Denial-of-service attacks

## Slide 49: Manageability
Performance management
Fault management
Configuration management
Security management
Accounting management

## Slide 50: Usability
Usability: the ease of use with which network users can access the network and services
Networks should make users’ jobs easier
Some design decisions will have a negative affect on usability:
  Strict security, for example

## Slide 51: Adaptability
Avoid incorporating any design elements that would make it hard to implement new technologies in the future
Change can come in the form of new protocols, new business practices, new fiscal goals, new legislation
A flexible design can adapt to changing traffic patterns and Quality of Service (QoS) requirements

## Slide 52: Affordability
A network should carry the maximum amount of traffic possible for a given financial cost
Affordability is especially important in campus network designs
WANs are expected to cost more, but costs can be reduced with the proper use of technology
  Quiet routing protocols, for example

## Slide 53: Network Applications Technical Requirements
Name of Application
Cost of Downtime
Acceptable MTBF
Acceptable MTTR
Throughput Goal
Delay Must be Less Than:
Delay Variation Must be Less Than:

## Slide 54: Making Tradeoffs
Scalability 20
Availability 30
Network performance 15
Security 5
Manageability 5
Usability 5
Adaptability 5
Affordability 15
Total (must add up to 100) 100

## Slide 55: Conclusion
Systematic approach
Focus first on business requirements and constraints, and applications
Gain an understanding of the customer’s corporate structure
Gain an understanding of the customer’s business style

## Slide 56: Conclusion (2)
Continue to use a systematic, top-down approach
Don’t select products until you understand goals for scalability, availability, performance, security, manageability, usability, adaptability, and affordability
Tradeoffs are almost always necessary

## Slide 57: DAFTAR PUSTAKA/SUMBER
Oppenheimer, Priscilla. (2013). Top Down Network Design. 3rd Edition. Cisco Press. Indianapolis. ISBN: 978-1-58705-152-4.
White, R., & Donohue, D. (2013). The Art of Network Architecture. Pearson Education.