## Slide 1: Network Governance SESSION 2 – Characterizing The Networks
D5727 – Dr. Eng. Nico Surantha, ST., MT.

## Slide 2: Outline
The health of existing internetwork
Characterizing traffic flow
Characterizing traffic load
Characterizing traffic behavior
Characterizing qoS Requirements

## Slide 3: What’s the Starting Point?
According to Abraham Lincoln:
  “If we could first know where we are and whither we are tending, we could better judge what to do and how to do it.”

## Slide 4: Where Are We?
Characterize the exiting internetwork in terms of:
  Its infrastructure
    Logical structure (modularity, hierarchy, topology)
    Physical structure
  Addressing and naming
  Wiring and media
  Architectural and environmental constraints
  Health

## Slide 5: Get a Network Map
Gigabit Ethernet
Eugene
Ethernet
20 users
Web/FTP server
Grants Pass
HQ
16 Mbps
Token Ring
FEP (Front End Processor)
IBM Mainframe
T1
Medford
Fast Ethernet
50 users
Roseburg
Fast Ethernet
30 users
Frame Relay
CIR = 56 Kbps
DLCI = 5
Frame Relay
CIR = 56 Kbps
DLCI = 4
Grants Pass
HQ
Fast Ethernet
75 users
Internet
T1

## Slide 6: Characterize Addressing and Naming
IP addressing for major devices, client networks, server networks, and so on
Any addressing oddities, such as discontiguous subnets?
Any strategies for addressing and naming?
  For example, sites may be named using airport codes
    San Francisco = SFO, Oakland = OAK

## Slide 7: Discontiguous Subnets
Area 1
Subnets 10.108.16.0 - 10.108.31.0
Area 0
Network 192.168.49.0
Area 2
Subnets 10.108.32.0 - 10.108.47.0
Router A
Router B

## Slide 8: Characterize the Wiring and Media
Single-mode fiber
Multi-mode fiber
Shielded twisted pair (STP) copper
Unshielded-twisted-pair (UTP) copper
Coaxial cable
Microwave
Laser
Radio
Infra-red

## Slide 9: Campus Network Wiring
Telecommunications
Wiring Closet
Horizontal
Wiring
Work-Area
Wiring
Wallplate
Main Cross-Connect Room
(or Main Distribution Frame)
Intermediate Cross-Connect Room
(or Intermediate Distribution Frame)
Building A - Headquarters
Building B
Vertical
Wiring
(Building
Backbone)
Campus
Backbone

## Slide 10: Architectural Constraints
Make sure the following are sufficient
  Air conditioning
  Heating
  Ventilation
  Power
  Protection from electromagnetic interference
  Doors that can lock

## Slide 11: Architectural Constraints
Make sure there’s space for:
  Cabling conduits
  Patch panels
  Equipment racks
  Work areas for technicians installing and troubleshooting equipment

## Slide 12: Issues for Wireless Installations
Reflection
Absorption
Refraction
Diffraction
Notes:     Reflection. Reflection causes the signal to bounce back on itself. The signal can interfere with itself in the air and affect the receiver’s ability to discriminate between the signal and noise in the environment. Reflection is caused by metal surfaces such as steel girders, scaffolding, shelving units, steel pillars, and metal doors. Implementing a Wireless LAN (WLAN) across a parking lot can be tricky because of metal cars that come and go.
    Absorption. Some of the electromagnetic energy of the signal can be absorbed by the material in objects through which it passes, resulting in a reduced signal level. Water has significant absorption properties, and objects such as trees or thick wooden structures can have a high water content. Implementing a WLAN in a coffee shop can be tricky if there are large canisters of liquid coffee. Coffee-shop WLAN users have also noticed that people coming and going can affect the signal level. (On StarTrek, a non-human character once called a human "a large, useless bag of mostly water!")
    Refraction. When an RF signal passes from a medium with one density into a medium with another density, the signal can be bent, much like light passing through a prism. The signal changes direction and may interfere with the non-refracted signal. It can take a different path and encounter other, unexpected obstructions, and arrive at recipients damaged or later than expected. As an example, a water tank not only introduces absorption, but the difference in density between the atmosphere and the water can bend the RF signal.
    Diffraction. Diffraction, which is similar to refraction, results when a region through which the RF signal can pass easily is adjacent to a region in which reflective obstructions exist. Like refraction, the RF signal is bent around the edge of the diffractive region and can then interfere with that part of the RF signal that is not bent.

## Slide 13: Check the Health of the Existing Internetwork
Performance
Availability
Bandwidth utilization
Accuracy
Efficiency
Response time
Status of major routers, switches, and firewalls

## Slide 14: Characterize Availability
 | MTBF | MTTR | Date and Duration of Last Major Downtime | Cause of Last Major Downtime
Enterprise |  |  |  | 
Segment 1 |  |  |  | 
Segment 2 |  |  |  | 
Segment n |  |  |  | 

## Slide 15: Network Utilization in Minute Intervals

## Slide 16: Network Utilization in Hour Intervals

## Slide 17: Bandwidth Utilization by Protocol
 | Relative Network Utilization | Absolute Network Utilization | Broadcast Rate | Multicast Rate
Protocol 1 |  |  |  | 
Protocol 2 |  |  |  | 
Protocol 3 |  |  |  | 
Protocol n |  |  |  | 
Notes: Relative usage specifies how much bandwidth is used by the protocol in comparison to the total bandwidth currently in use on the segment. Absolute usage specifies how much bandwidth is used by the protocol in comparison to the total capacity of the segment (for example, in comparison to 100 Mbps on Fast Ethernet).

## Slide 18: Characterize Packet Sizes

## Slide 19: Characterize Response Time
X
X
 | Node A | Node B | Node C | Node D
Node A | X |  |  | 
Node B |  | X |  | 
Node C |  |  | X | 
Node D |  |  |  | X

## Slide 20: Check the Status of Major Routers, Switches, and Firewalls
show buffers
show environment
show interfaces
show memory
show processes
show running-config
show version

## Slide 21: Tools
Protocol analyzers
Multi Router Traffic Grapher (MRTG)
Remote monitoring (RMON) probes
Cisco Discovery Protocol (CDP)
Cisco IOS NetFlow technology
CiscoWorks
Cisco IOS Service Assurance Agent (SAA)
Cisco Internetwork Performance Monitor (IPM)

## Slide 22: User Communities
User Community Name | Size of Community (Number of Users) | Location(s) of Community | Application(s) Used by Community

## Slide 23: Data Stores
Data Store
Location
Application(s)
Used by User Community(or Communities)

## Slide 24: Traffic Flow
 | Destination 1 MB/sec | Destination 2 MB/sec | Destination 3 MB/sec | Destination MB/sec
Source 1 |  |  |  | 
Source 2 |  |  |  | 
Source 3 |  |  |  | 
Source n |  |  |  | 

## Slide 25: Traffic Flow Example
Administration
Business and Social Sciences
Math and Sciences
50 PCs
25 Macs
50 PCs
50 PCs
30 PCs
30 Library Patrons (PCs)
30 Macs and 60 PCs in Computing Center
Library and Computing Center
App 1 108 Kbps
App 2 60 Kbps
App 3 192 Kbps
App 4 48 Kbps
App 7 400 Kbps
Total 808 Kbps
App 1 48 Kbps
App 2 32 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 5 300 Kbps
App 6 200 Kbps
App 8 1200 Kbps
Total 1900 Kbps
App 1 30 Kbps
App 2 20 Kbps
App 3 60 Kbps
App 4 16 Kbps
Total 126 Kbps
App 2 20 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 9 80 Kbps
Total 220 Kbps
Arts and Humanities
Server Farm
10-Mbps Metro Ethernet to Internet

## Slide 26: Types of Traffic Flow
Terminal/host
Client/server
Thin client
Peer-to-peer
Server/server
Distributed computing

## Slide 27: Traffic Flow for Voice over IP
The flow associated with transmitting the audio voice is separate from the flows associated with call setup and teardown.
  The flow for transmitting the digital voice is essentially peer-to-peer.
  Call setup and teardown is a client/server flow
    A phone needs to talk to a server or phone switch that understands phone numbers, IP addresses, capabilities negotiation, and so on.

## Slide 28: Network Applications Traffic Characteristics
Name of Application | Type of Traffic Flow | Protocol(s) Used by Application | User Communities That Use the Application | Data Stores (Servers, Hosts, and so on) | Approximate Bandwidth Requirements | QoS Requirements

## Slide 29: Traffic Load
To calculate whether capacity is sufficient, you should know:
  The number of stations
  The average time that a station is idle between sending frames
  The time required to transmit a message once medium access is gained
That level of detailed information can be hard to gather, however

## Slide 30: Size of Objects on Networks
Terminal screen: 4 Kbytes
Simple e-mail: 10 Kbytes
Simple web page: 50 Kbytes
High-quality image: 50,000 Kbytes
Database backup: 1,000,000 Kbytes or more

## Slide 31: Traffic Behavior
Broadcasts
  All ones data-link layer destination address
    FF: FF: FF: FF: FF: FF
  Doesn’t necessarily use huge amounts of bandwidth
  But does disturb every CPU in the broadcast domain
Multicasts
  First bit sent is a one
    01:00:0C:CC:CC:CC (Cisco Discovery Protocol)
  Should just disturb NICs that have registered to receive it
  Requires multicast routing protocol on internetworks

## Slide 32: Network Efficiency
Frame size
Protocol interaction
Windowing and flow control
Error-recovery mechanisms

## Slide 33: QoS Requirements
ATM service specifications
  Constant bit rate (CBR)
  Realtime variable bit rate (rt-VBR)
  Non-realtime variable bit rate (nrt-VBR)
  Unspecified bit rate (UBR)
  Available bit rate (ABR)
  Guaranteed frame rate (GFR)

## Slide 34: QoS Requirements per IETF
IETF integrated services working group specifications
  Controlled load service
    Provides client data flow with a QoS closely approximating the QoS that same flow would receive on an unloaded network
  Guaranteed service
    Provides firm (mathematically provable) bounds on end-to-end packet-queuing delays

## Slide 35: QoS Requirements per IETF
IETF differentiated services working group specifications
  RFC 2475
  IP packets can be marked with a differentiated services codepoint (DSCP) to influence queuing and packet-dropping decisions for IP datagrams on an output interface of a router

## Slide 36: Network Traffic Factors
Traffic flow
Location of traffic sources and data stores
Traffic load
Traffic behavior
Quality of Service (QoS) requirements

## Slide 37: Conclusion
Characterize the exiting internetwork before designing enhancements
Helps you verify that a customer’s design goals are realistic
Helps you locate where new equipment will go
Helps you cover yourself if the new network has problems due to unresolved problems in the old network

## Slide 38: Conclusion (2)
Continue to use a systematic, top-down approach
Don’t select products until you understand network traffic in terms of:
  Flow
  Load
  Behavior
  QoS requirements

## Slide 39: DAFTAR PUSTAKA/SUMBER
Oppenheimer, Priscilla. (2013). Top Down Network Design. 3rd Edition. Cisco Press. Indianapolis. ISBN: 978-1-58705-152-4.
White, R., & Donohue, D. (2013). The Art of Network Architecture. Pearson Education.