## Slide 1: Network Governance SESSION 3 – Designing Network Topology
D5727 – Dr. Eng. Nico Surantha, ST., MT.

## Slide 2: Outline
HIErarchical Network design
Redundant Network Design Topologies
Modular Network Design
Designing a Campus Network Design Topology
Designing the Enterprise Edge Topology
Secure Network Design Topologies

## Slide 3: Topology
A branch of mathematics concerned with those properties of geometric configurations that are unaltered by elastic deformations such as stretching or twisting
A term used in the computer networking field to describe the structure of a network
Notes: Did you know that according to topologists, a coffee cup and donut are the same shape? If they were made of clay, for example, consider how easy it would be to mold the one to look like the other, while retaining the most significant characteristics (such as the roundedness and the hole).
Just like with coffee and donuts made of clay, in the networking field, during the logical design phase, we are more concerned with the overall architecture, shape, size, and interconnectedness of a network, than with the physical details.
For more information regarding topology, coffee, and donuts, see:
http://en.wikipedia.org/wiki/Topology
and
http://msl.cs.uiuc.edu/planning/node93.html

## Slide 4: Network Topology Design Themes
Hierarchy
Redundancy
Modularity
Well-defined entries and exits
Protected perimeters

## Slide 5: Why Use a Hierarchical Model?
Reduces workload on network devices
  Avoids devices having to communicate with too many other devices (reduces “CPU adjacencies”)
Constrains broadcast domains
Enhances simplicity and understanding
Facilitates changes
Facilitates scaling to a larger size

## Slide 6: Hierarchical Network Design
Distribution Layer
Enterprise WAN
Backbone
Campus A
Campus B
Campus C
Building C-1
Building C-2
Campus C Backbone
Core Layer
Access Layer

## Slide 7: Cisco’s Hierarchical Design Model
A core layer of high-end routers and switches that are optimized for availability and speed
A distribution layer of routers and switches that implement policies and segment traffic
An access layer that connects users via hubs, switches, and other devices

## Slide 8: Flat Versus Hierarchy
Flat Loop Topology
Headquarters in Medford
Grants Pass Branch Office
Ashland Branch Office
Klamath Falls Branch Office
Headquarters in Medford
Ashland Branch Office
Klamath Falls Branch Office
Grants Pass Branch Office
White City Branch Office
Hierarchical Redundant Topology

## Slide 9: Mesh Designs
Partial-Mesh Topology
Full-Mesh Topology

## Slide 10: A Partial-Mesh Hierarchical Design
Branch Offices (Access Layer)
Headquarters (Core Layer)
Regional Offices (Distribution Layer)

## Slide 11: A Hub-and-Spoke Hierarchical Topology
Branch Office
Corporate Headquarters
Branch Office
Home Office

## Slide 12: Avoid Chains and Backdoors
Core Layer
Distribution Layer
Access Layer
Chain
Backdoor

## Slide 13: How Do You Know When You Have a Good Design?
When you already know how to add a new building, floor, WAN link, remote site, e-commerce service, and so on
When new additions cause only local change, to the directly-connected devices
When your network can double or triple in size without major design changes
When troubleshooting is easy because there are no complex protocol interactions to wrap your brain around
Notes: Said by Dr. Peter Welcher, consultant and author of many networking articles in magazines, etc.

## Slide 14: Cisco’s Enterprise Composite Network Model
Network
Management
Building
Access
Building
Distribution
Campus
Backbone
Server Farm
Edge
Distribution
E-Commerce
Internet
Connectivity
VPN/ Remote
Access
WAN
ISP A
ISP B
PSTN
Frame
Relay,
ATM
Campus Infrastructure
Enterprise Campus
Enterprise Edge
Service Provider Edge

## Slide 15: Campus Topology Design
Use a hierarchical, modular approach
Minimize the size of bandwidth domains
Minimize the size of broadcast domains
Provide redundancy
  Mirrored servers
  Multiple ways for workstations to reach a router for off-net communications

## Slide 16: Enterprise Campus Modules
Server farm
Network management module
Edge distribution module for connectivity to the rest of the world
Campus infrastructure module:
  Building access submodule
  Building distribution submodule
  Campus backbone
Notes:     Building access submodule. Located within a campus building, this submodule contains end-user workstations and IP phones, connected to switches or wireless access points. Higher-end switches provide uplinks to the building distribution module. Services offered by this module include network access, broadcast control, protocol filtering, and the marking of packets for QoS features.
    Building distribution submodule. The job of this submodule is to aggregate wiring closets within a building and provide connectivity to the campus backbone via routers (or switches with routing modules). This submodule provides routing, QoS, and access control methods for meeting security and performance requirements. Redundancy and load sharing are recommended for this submodule. For example, each building distribution submodule should have two equal-cost paths to the campus backbone.
    Campus backbone. The campus backbone is the core layer of the campus infrastructure. The backbone interconnects the building access and distribution submodules with the server farm, network management, and edge distribution modules. The campus backbone provides redundant and fast-converging connectivity. It routes and switches traffic as fast quickly as possible from one module to another. This module usually uses high-speed routers (or switches with routing capability) and provides QoS and security features.

## Slide 17: A Simple Campus Redundant Design
Host A
Host B
LAN X
LAN Y
Switch 1
Switch 2

## Slide 18: Bridges and Switches use Spanning-Tree Protocol (STP) to Avoid Loops
X
Host A
Host B
LAN X
LAN Y
Switch 1
Switch 2

## Slide 19: Bridges (Switches) Running STP
Participate with other bridges in the election of a single bridge as the Root Bridge.
Calculate the distance of the shortest path to the Root Bridge and choose a port (known as the Root Port) that provides the shortest path to the Root Bridge.
For each LAN segment, elect a Designated Bridge and a Designated Port on that bridge. The Designated Port is a port on the LAN segment that is closest to the Root Bridge. (All ports on the Root Bridge are Designated Ports.)
Select bridge ports to be included in the spanning tree. The ports selected are the Root Ports and Designated Ports. These ports forward traffic. Other ports block traffic.
Notes: If all ports have equal distance to the Root Bridge, then the Designated Port is chosen by lowest sender Bridge ID. If the IDs are the same, then the port is chosen by lowest Port ID.
In general, STP checks for the best information by using these four criteria in the following order:
Lowest Root Bridge ID
Lowest path cost to the Root Bridge
Lowest sender Bridge ID
Lowest Port ID
See Top-Down Network Design for more details.

## Slide 20: Elect a Root
Bridge B
Bridge C
Bridge A ID = 80.00.00.00.0C.AA.AA.AA
Bridge B ID = 80.00.00.00.0C.BB.BB.BB
Bridge C ID = 80.00.00.00.0C.CC.CC.CC
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
LAN Segment 2
100-Mbps Ethernet
Cost = 19
LAN Segment 1
100-Mbps Ethernet
Cost = 19
LAN Segment 3
100-Mbps Ethernet
Cost = 19
Root
Bridge A
Lowest Bridge ID
Wins!
Bridges (Switches) Running STP

## Slide 21: Determine Root Ports
Bridge B
Bridge C
Root
Bridge A
Bridge A ID = 80.00.00.00.0C.AA.AA.AA
Bridge B ID = 80.00.00.00.0C.BB.BB.BB
Bridge C ID = 80.00.00.00.0C.CC.CC.CC
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
LAN Segment 2
100-Mbps Ethernet
Cost = 19
LAN Segment 1
100-Mbps Ethernet
Cost = 19
LAN Segment 3
100-Mbps Ethernet
Cost = 19
Root Port
Root Port
Lowest Cost
Wins!
Bridges (Switches) Running STP

## Slide 22: Determine Designated Ports
Bridge B
Bridge C
Root
Bridge A
Bridge A ID = 80.00.00.00.0C.AA.AA.AA
Bridge B ID = 80.00.00.00.0C.BB.BB.BB
Bridge C ID = 80.00.00.00.0C.CC.CC.CC
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
LAN Segment 2
100-Mbps Ethernet
Cost = 19
LAN Segment 1
100-Mbps Ethernet
Cost = 19
LAN Segment 3
100-Mbps Ethernet
Cost = 19
Root Port
Root Port
Designated Port
Designated Port
Designated Port
Lowest Bridge ID
Wins!
Bridges (Switches) Running STP

## Slide 23: Prune Topology into a Tree!
Bridge B
Bridge C
Root
Bridge A
Bridge A ID = 80.00.00.00.0C.AA.AA.AA
Bridge B ID = 80.00.00.00.0C.BB.BB.BB
Bridge C ID = 80.00.00.00.0C.CC.CC.CC
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
LAN Segment 2
100-Mbps Ethernet
Cost = 19
LAN Segment 1
100-Mbps Ethernet
Cost = 19
LAN Segment 3
100-Mbps Ethernet
Cost = 19
Root Port
Root Port
Designated Port
Designated Port
Designated Port
Blocked Port
X
Bridges (Switches) Running STP

## Slide 24: React to Changes
Bridge B
Bridge C
Root
Bridge A
Bridge A ID = 80.00.00.00.0C.AA.AA.AA
Bridge B ID = 80.00.00.00.0C.BB.BB.BB
Bridge C ID = 80.00.00.00.0C.CC.CC.CC
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
LAN Segment 2
LAN Segment 1
LAN Segment 3
Root Port
Root Port
Designated Port
Designated Port
Designated Port Becomes Disabled
Blocked Port Transitions to Forwarding State
Bridges (Switches) Running STP

## Slide 25: Scaling the Spanning Tree Protocol
Keep the switched network small
  It shouldn’t span more than seven switches
Use BPDU skew detection on Cisco switches
Use IEEE 802.1w
  Provides rapid reconfiguration of the spanning tree
  Also known as RSTP

## Slide 26: Virtual LANs (VLANs)
An emulation of a standard LAN that allows data transfer to take place without the traditional physical restraints placed on a network
A set of devices that belong to an administrative group
Designers use VLANs to constrain broadcast traffic

## Slide 27: VLANs versus Real LANs
Switch A
Station A1
Station A2
Station A3
Network A
Switch B
Station B1
Station B2
Station B3
Network B
Notes: To understand VLANs, it helps to think about real (non-virtual) LANs first. Imagine two switches that are not connected to each other in any way. Switch A connects stations in Network A and Switch B connects stations in Network B,
When Station A1 sends a broadcast, Station A2 and Station A3 receive the broadcast, but none of the stations in Network B receive the broadcast, because the two switches are not connected. This same configuration can be implemented through configuration options in a single switch, with the result looking like the next slide.

## Slide 28: A Switch with VLANs
Station A1
Station A2
Station A3
VLAN A
Station B1
Station B2
Station B3
VLAN B
VLANs versus Real LANs
Notes: Through the configuration of the switch there are now two virtual LANs implemented in a single switch, instead of two separate physical LANs. This is the beauty of VLANs. The broadcast, multicast, and unknown-destination traffic originating with any member of VLAN A is forwarded to all other members of VLAN A, and not to a member of VLAN B. VLAN A has the same properties as a physically separate LAN bounded by routers. The protocol behavior in this slide is exactly the same as the protocol behavior in the previous slide.

## Slide 29: VLANs Span Switches
Switch A
Station B1
Station B2
Station B3
Switch B
Station B4
Station B5
Station B6
Station A1
Station A2
Station A3
Station A4
Station A5
Station A6
VLAN B
VLAN A
VLAN B
VLAN A
Notes: VLANs can span multiple switches. In this slide, both switches contain stations that are members of VLAN A and VLAN B. This design introduces a new problem, the solution to which is specified in the IEEE 802.1Q standard and the Cisco proprietary Inter-Switch Link (ISL) protocol. The problem has to do with the forwarding of broadcast, multicast, or unknown-destination frames from a member of a VLAN on one switch to the members of the same VLAN on the other switch.
In this slide, all frames going from Switch A to Switch B take the same interconnection path. The 802.1Q standard and Cisco's ISL protocol define a method for Switch B to recognize whether an incoming frame belongs to VLAN A or to VLAN B. As a frame leaves Switch A, a special header is added to the frame, called the VLAN tag. The VLAN tag contains a VLAN identifier (ID) that specifies to which VLAN the frame belongs.
Because both switches have been configured to recognize VLAN A and VLAN B, they can exchange frames across the interconnection link, and the recipient switch can determine the VLAN into which those frames should be sent by examining the VLAN tag. The link between the two switches is sometimes called a trunk link or simply a trunk.
Trunk links allow the network designer to stitch together VLANs that span multiple switches. A major design consideration is determining the scope of each VLAN and how many switches it should span. Most designers try to keep the scope small. Each VLAN is a broadcast domain. In general, a single broadcast domain should be limited to a few hundred workstations (or other devices, such as IP phones).

## Slide 30: WLANs and VLANs
A wireless LAN (WLAN) is often implemented as a VLAN
Facilitates roaming
Users remain in the same VLAN and IP subnet as they roam, so there’s no need to change addressing information
Also makes it easier to set up filters (access control lists) to protect the wired network from wireless users

## Slide 31: Workstation-to-Router Communication
Proxy ARP (not a good idea)
Listen for route advertisements (not a great idea either)
ICMP router solicitations (not widely used)
Default gateway provided by DHCP (better idea but no redundancy)
  Use Hot Standby Router Protocol (HSRP) for redundancy

## Slide 32: HSRP
Active Router
Standby Router
Virtual Router
Workstation
Enterprise Internetwork

## Slide 33: Multihoming the Internet Connection
Enterprise
Enterprise
Enterprise
ISP 1
ISP 1
ISP 2
ISP 1
ISP 1
ISP 2
Enterprise
Option A
Option B
Option C
Option D
Paris
NY
Paris
NY

## Slide 34: Security Topologies
Enterprise
Network
DMZ
Web, File, DNS, Mail Servers
Internet

## Slide 35: Security Topologies
Internet
Enterprise Network
DMZ
Web, File, DNS, Mail Servers
Firewall
Security Topologies

## Slide 36: Summary
Use a systematic, top-down approach
Plan the logical design before the physical design
Topology design should feature hierarchy, redundancy, modularity, and security

## Slide 37: DAFTAR PUSTAKA/SUMBER
Oppenheimer, Priscilla. (2013). Top Down Network Design. 3rd Edition. Cisco Press. Indianapolis. ISBN: 978-1-58705-152-4.
Hummel, S. L. (2015). Cisco Design Fundamentals: Multilayered Network Architecture and Design for Network Engineers.