## Slide 1: Network Governance SESSION 5 – Selecting Switching and Routing Protocols
D5727 – Dr. Eng. Nico Surantha, ST., MT.

## Slide 2: Outline
Selecting Switching Protocols
Selecting Routing Protocols
IP Routing
Using Multiple Routing Protocols in an Internetwork

## Slide 3: Switching and Routing Choices
Switching
  Layer 2 transparent bridging (switching)
  Multilayer switching
  Spanning Tree Protocol enhancements
  VLAN technologies
Routing
  Static or dynamic
  Distance-vector and link-state protocols
  Interior and exterior
  Etc.

## Slide 4: Selection Criteria for Switching and Routing Protocols
Network traffic characteristics
Bandwidth, memory, and CPU usage
The number of peers supported
The capability to adapt to changes quickly
Support for authentication

## Slide 5: Making Decisions
Goals must be established
Many options should be explored
The consequences of the decision should be investigated
Contingency plans should be made
A decision table can be used

## Slide 6: Example Decision Table

## Slide 7: Transparent Bridging (Switching) Tasks
Forward frames transparently
Learn which port to use for each MAC address
Flood frames when the destination unicast address hasn’t been learned yet
Filter frames from going out ports that don’t include the destination address
Flood broadcasts and multicasts

## Slide 8: Switching Table on a Bridge or Switch
MAC Address
Port
1
2
3
08-00-07-06-41-B9
00-00-0C-60-7C-01
00-80-24-07-8C-02

## Slide 9: Cisco Multilayer Switching
Route processor or router
Switching engine
The Multilayer Switching Protocol (MLSP)

## Slide 10: Cisco Spanning Tree Protocol Enhancements
PortFast
UplinkFast and Backbone Fast
Unidirectional link detection
Loop Guard

## Slide 11: Redundant Uplinks
Access Layer
Distribution Layer
Core
Layer
Switch A
Switch B
Switch C
Primary Uplink
Secondary Uplink
X
X
X = blocked by STP
If a link fails, how long will STP take to recover?
Use UplinkFast to speed convergence

## Slide 12: Protocols for Transporting VLAN Information
Inter-Switch Link (ISL)
  Tagging protocol
  Cisco proprietary
IEEE 802.1Q
  Tagging protocol
  IEEE standard
VLAN Trunk Protocol (VTP)
  VLAN management protocol

## Slide 13: Selecting Routing Protocols
They all have the same general goal:
  To share network reachability information among routers
They differ in many ways:
  Interior versus exterior
  Metrics supported
  Dynamic versus static and default
  Distance-vector versus link-sate
  Classful versus classless
  Scalability

## Slide 14: Interior Versus Exterior Routing Protocols
Interior routing protocols are used within an autonomous system
Exterior routing protocols are used between autonomous systems
Autonomous system (two definitions that are often used):
“A set of routers that presents a common routing policy to the internetwork”
“A network or set of networks that are under the administrative control of a single entity”

## Slide 15: Routing Protocol Metrics
Metric: the determining factor used by a routing algorithm to decide which route to a network is better than another
Examples of metrics:
  Bandwidth - capacity
  Delay - time
  Load - amount of network traffic
  Reliability - error rate
  Hop count - number of routers that a packet must travel through before reaching the destination network
  Cost - arbitrary value defined by the protocol or administrator

## Slide 16: Routing Algorithms
Static routing
  Calculated beforehand, offline
Default routing
  “If I don’t recognize the destination, just send the packet to Router X”
Cisco’s On-Demand Routing
  Routing for stub networks
  Uses Cisco Discovery Protocol (CDP)
Dynamic routing protocol
  Distance-vector algorithms
  Link-state algorithms

## Slide 17: Static Routing Example
RouterA(config)#ip route 172.16.50.0 255.255.255.0 172.16.20.2
Send packets for subnet 50 to 172.16.20.2 (Router B)
e0
e0
e0
s0
s1
s0
s0
Router A
Router B
Router C
Host A
Host C
Host B
172.16.10.2
172.16.30.2
172.16.50.2
172.16.20.1
172.16.40.1
172.16.10.1
172.16.30.1
172.16.50.1
172.16.20.2
172.16.40.2

## Slide 18: Default Routing Example
RouterA(config)#ip route 0.0.0.0 0.0.0.0 172.16.20.2
If it’s not local, send it to 172.16.20.2 (Router B)
e0
e0
e0
s0
s1
s0
s0
Router A
Router B
Router C
Host A
Host C
Host B
172.16.10.2
172.16.30.2
172.16.50.2
172.16.20.1
172.16.40.1
172.16.10.1
172.16.30.1
172.16.50.1
172.16.20.2
172.16.40.2

## Slide 19: Distance-Vector Routing
Router maintains a routing table that lists known networks, direction (vector) to each network, and the distance to each network
Router periodically (every 30 seconds, for example) transmits the routing table via a broadcast packet that reaches all other routers on the local segments
Router updates the routing table, if necessary, based on received broadcasts

## Slide 20: Distance-Vector Routing Tables
Router A
Router B
172.16.0.0
192.168.2.0
Network Distance Send To
172.16.0.0 0 Port 1
192.168.2.0 1 Router B
Network Distance Send To
192.168.2.0 0 Port 1 172.16.0.0 1 Router A
Router A’s Routing Table
Router B’s Routing Table

## Slide 21: Link-State Routing
Routers send updates only when there’s a change
Router that detects change creates a link-state advertisement (LSA) and sends it to neighbors
Neighbors propagate the change to their neighbors
Routers update their topological database if necessary

## Slide 22: Distance-Vector Vs. Link-State
Distance-vector algorithms keep a list of networks, with next hop and distance (metric) information
Link-state algorithms keep a database of routers and links between them
  Link-state algorithms think of the internetwork as a graph instead of a list
  When changes occur, link-state algorithms apply Dijkstra’s shortest-path algorithm to find the shortest path between any two nodes

## Slide 23: Choosing Between Distance-Vector and Link-State
Choose Distance-Vector
Simple, flat topology
Hub-and-spoke topology
Junior network administrators
Convergence time not a big concern
Choose Link-State
Hierarchical topology
More senior network administrators
Fast convergence is critical

## Slide 24: Dynamic IP Routing Protocols
Distance-Vector
Routing Information Protocol (RIP) Version 1 and 2
Interior Gateway Routing Protocol (IGRP)
Enhanced IGRP
Border Gateway Protocol (BGP)
Link-State
Open Shortest Path First (OSPF)
Intermediate System-to-Intermediate System (IS-IS)

## Slide 25: Routing Information Protocol (RIP)
First standard routing protocol developed for TCP/IP environments
  RIP Version 1 is documented in RFC 1058 (1988)
  RIP Version 2 is documented in RFC 2453 (1998)
Easy to configure and troubleshoot
Broadcasts its routing table every 30 seconds; 25 routes per packet
Uses a single routing metric (hop count) to measure the distance to a destination network; max hop count is 15

## Slide 26: RIP V2 Features
Includes the subnet mask with route updates
  Supports prefix routing (classless routing, supernetting)
  Supports variable-length subnet masking (VLSM)
Includes simple authentication to foil crackers sending routing updates

## Slide 27: IGRP Solved Problems with RIP
15-hop limitation in RIP
  IGRP supports 255 hops
Reliance on just one metric (hop count)
  IGRP uses bandwidth, delay, reliability, load
  (By default just uses bandwidth and delay)
RIP's 30-second update timer
  IGRP uses 90 seconds

## Slide 28: EIGRP
Adjusts to changes in internetwork very quickly
Incremental updates contain only changes, not full routing table
Updates are delivered reliably
Router keeps track of neighbors’ routing tables and uses them as feasible successor
Same metric as IGRP, but more granularity (32 bits instead of 24 bits)

## Slide 29: Open Shortest Path First (OSPF)
Open standard, defined in RFC 2328
Adjusts to changes quickly
Supports very large internetworks
Does not use a lot of bandwidth
Authenticates protocol exchanges to meet security goals

## Slide 30: OSPF Metric
A single dimensionless value called cost. A network administrator assigns an OSPF cost to each router interface on the path to a network. The lower the cost, the more likely the interface is to be used to forward data traffic.
On a Cisco router, the cost of an interface defaults to 100,000,000 divided by the bandwidth for the interface. For example, a 100-Mbps Ethernet interface has a cost of 1.

## Slide 31: OSPF Areas Connected via Area Border Routers (ABRs)
Area 1
Area 3
Area 2
Area 0 (Backbone)
ABR
ABR
ABR

## Slide 32: IS-IS
Intermediate System-to-Intermediate System
Link-state routing protocol
Designed by the ISO for the OSI protocols
Integrated IS-IS handles IP also

## Slide 33: Border Gateway Protocol (BGP)
Allows routers in different autonomous systems to exchange routing information
  Exterior routing protocol
  Used on the Internet among large ISPs and major companies
Supports route aggregation
Main metric is the length of the list of autonomous system numbers, but BGP also supports routing based on policies

## Slide 34: Summary
The selection of switching and routing protocols should be based on an analysis of
  Goals
  Scalability and performance characteristics of the protocols
Transparent bridging is used on modern switches
  But other choices involve enhancements to STP and protocols for transporting VLAN information
There are many types of routing protocols and many choices within each type
Conclusion

## Slide 35: DAFTAR PUSTAKA/SUMBER
Oppenheimer, Priscilla. (2013). Top Down Network Design. 3rd Edition. Cisco Press. Indianapolis. ISBN: 978-1-58705-152-4.
White, R., & Donohue, D. (2013). The Art of Network Architecture. Pearson Education.