## Slide 1: ARSITEKTUR KOMPUTER PERTEMUAN 6

## Slide 2
Recall: Chapter 4 – Common Memory Parameters
Memory Type | Technology | Size | Access Time
Cache | Semiconductor RAM | 128-512 KB | 10 ns
Main Memory | Semiconductor RAM | 4-128 MB | 50 ns
Magnetic Disk | Hard Disk | Gigabyte | 10 ms,10 MB/sec
Optical Disk | CD-ROM | Gigabyte | 300 ms, 600 KB/sec
Magnetic Tape | Tape | 100s MB | Sec-min.,10MB/min

## Slide 3
Types of External Memory
Magnetic Disk
Optical
Magnetic Tape

## Slide 4
Magnetic Disk

## Slide 5
Magnetic Disk
Disk
  A circular platter constructed of nonmagnetic material called substrate
    Aluminium (old)
    Glass (new)
  Coated with a magnetisable material

## Slide 6
Magnetic Disk (Cont.)
Glass
  Improved surface uniformity
    Increases reliability
  Reduction in surface defects
    Reduced read/write errors
  Better stiffness – to reduce disk dynamics
  Greater ability to withstand shock and damage

## Slide 7
Magnetic Disk – Read/Write
Mechanisms
  Recording & retrieval via conductive coil called a head
  May be single read/write head or separate ones
  During read/write, head is stationary, platter rotates

## Slide 8
Magnetic Disk – Read/Write (Cont.)
Write
Current through coil produces magnetic field
Pulses sent to head
Magnetic pattern recorded on surface below
Read
Traditional
  Magnetic field moving relative to coil produces current
  Coil is the same for read and write
Contemporary
  Separate read head, close to write head
  Partially shielded magneto resistive (MR) sensor
  Electrical resistance depends on direction of magnetic field
  High frequency operation
    Higher storage density and speed

## Slide 9
Magnetic Disk – Organization, Formatting & Layout
Term | Description
Head | A small device capable of reading from or writing to a portion of the platter rotating beneath it
Track | Organize data on the platter in a concentric set of rings
Width | Track width = head width
Gaps | separate the adjacent tracks
Sectors | Form of transferring the data Fixed length or variable length

## Slide 10
Magnetic Disk - Velocity
Issue: Bit near centre of rotating disk passes fixed point slower than bit on outside of disk
Solution:
  Increasing the spacing between bits of information recorded in segments of the disk
  The info can then be scanned at the same rate by rotating the disk at a fixed speed known as constant angular velocity (CAV)

## Slide 11
Magnetic Disk - Layout Methods Diagram

## Slide 12
Magnetic Disk – Constant Angular Velocity
The disk is divided into a number of pie-shaped sectors and into a series of concentric tracks
Advantage of CAV:
  The individual blocks of data can be directly addressed by tracks and sectors
Disadvantage of CAV:
  The amount of data that can be stored on the long outer tracks is the only same as what can be stored on the short inner tracks

## Slide 13
Magnetic Disk – Multiple Zone Recording
The surface is divided into a number of concentric zones –
  The number of bits per track is constant (Within the zone)
  Zones farther from the center contain more bits (since more sectors) than zones closer to the center
Advantage:
  Increase density
Disadvantage:
  Require complex circuitry

## Slide 14
Magnetic Disk – Physical Characteristics
Head motion
  Fixed head
    One read write head per track
    Heads mounted on fixed ridged arm
  Movable head
    One read write head per side
    Mounted on a movable arm

## Slide 15
Magnetic Disk – Physical Characteristics (Cont.)
Removable disk
  Can be removed from drive and replaced with another disk
  Provides unlimited storage capacity
  Easy data transfer between systems
Non-removable disk
  Permanently mounted in the drive

## Slide 16
Magnetic Disk – Physical Characteristics (Cont.)
Multiple Platter
  One head per side
  Heads are joined and aligned
  Aligned tracks on each platter form cylinders
  Data is striped by cylinder
    Reduces head movement
    Increases speed (transfer rate)

## Slide 17
Magnetic Disk – Physical Characteristics (Cont.)
Tracks and Cylinders

## Slide 18
Magnetic Disk – Classifications
Head mechanism
#1 Traditional head
  Positioned a fixed distance above the platter-allowing an air gap
#2 head mechanism that actually comes into physical contact with the medium during R/W operation
  Used in floppy disk
    8”, 5.25”, 3.5”
    Small capacity
    Up to 1.44Mbyte (2.88M never popular)
    Slow
    Universal
    Cheap

## Slide 19
Magnetic Disk – Classifications (Cont.)
Head mechanism
#3 Winchester
  Aerodynamic gap
  Generate or sense an electromagnetic field of sufficient magnitude - write/read
  Used in sealed drive – free of contamination – able to reduce the risk of error
  Operate closer to the disk’s surface  greater data density
  Material - Aerodynamic foil - rests lightly on the platter’s surface

## Slide 20
Magnetic Disk - Performance
Depends on;
  Computer system
  OS
  Nature of the I/O channel
  Disk controller hardware

## Slide 21
Magnetic Disk – Performance (Cont.)
General timing of disk I/O transfer
Seek time  Moving head to correct track
(Rotational) latency/delay  Waiting for data to rotate under head
Access time = Seek + Latency
Transfer rate-the time required for the transfer data